## Slide 1: Paving the Path for Heterogeneous Memory Adoption in Production Systems
Neha Agarwal
Chair: Thomas F. Wenisch
Defense, Feb 20, 2017
Notes: Hi Everyone, I am Neha and today I will present data management policies that can simplify the design of otherwise complex heterogeneous systems improving programmability of the system while meeting application performance requirements.
I will be presenting my work on heterogeneous memory system design.

## Slide 2: Heterogeneous memory systems
Found everywhere: supercomputers, data-centers, cloud-services
+
Notes: Talk about heterogeneous memories here. We can find heterogeneous memory systems from fastest supercomputers to cloud services. For example, Titan a supercomputer built at Oak Ridge National Lab comprises of GPUs and Xeon Phis alongside of CPUs. Similarly, there is an emerging trend of deploying GPUs to accelerate machine learning applications in data-centers and cloud platforms. But let’s first understand why build a heterogeneous system in the first place.

## Slide 3: Why build heterogeneous systems?
Goal: increase performance per unit cost
  Increase performance; accelerate applications ➤ less CPU time
  Decrease cost; cost of ownership, programmers, design, verification
Applications are different in nature
  Have different memory access patterns: streaming, random
  Latency-sensitive, bandwidth-sensitive
Match application to a computing platform / memory technology
Notes: The main goal of designing any computing platform or stack is to maximize performance for every dollar spent. Increasing performance means that we want to run our applications faster than before. With specialized accelerators like throughput-oriented GPUs we have been able to cut down on computing time by orders of magnitude. Another parameter of our metric is cost, which can comprise of cost of owning and maintaining a computing facility, cost of hiring programmers, cost of designing and verifying a machine, which may not be directly quantifiable, but is a significant contributor to the overall cost. But, why not design a single machine to optimize for all these variables.
It turns out that all applications we want to run are not the same. Heterogeneity is a feature that applications exhibit in terms of different memory access patterns, some may be latency-sensitive like customer facing apps, or some can be bandwidth-sensitive instead for example data analytics crunching numbers out of a day long log of Uber rides.
So, in order to increase perf/dollar we need to match application nature with the available computing platforms or memory technologies or design new ones. The focus of my research is to design exploit heterogeneity in main memory technologies to drive up perf/dollar of computing platforms.

## Slide 4: Heterogeneity in memory technologies
Memory Technology | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
GDDR / HBM | 1x | 2x-8x | 2x | 2x
3D XPoint (expected) | 5x-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
Most servers/desktops have DDR main memory
Notes: So, lets look at different memory technologies that exhibit different characteristics in terms of access latency, bandwidth, cost/bit etc. In this table, DDR technology is the most popular one that can be found in all our laptops, commonly referred as RAM or DRAM.

## Slide 5: Heterogeneity in memory technologies
Memory Technology | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
GDDR / HBM | 1x | 2x-8x | 2x | 2x
3D XPoint (expected) | 5x-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
5x - 10x
How to exploit characteristics of different memory technologies?
High bandwidth memory
Cheaper slower memory
2x - 8x
x/3 - x/5
GDDR/HBM
3D XPoint
GPUs are massively parallel thus need lot of bandwidth, hence have high bandwidth memories
Upcoming memory technology by Intel/Micron
Notes: In comparison to DDR technology we can see that the GDDR technology is a high bandwidth memory whose bandwidth can be as high as 8x of that DDRs. Turns out that high performance computing applications like fluid dynamics simulations etc. require tones of bandwidth to process different flows that can be done parallely. Thus, GDDR matches the requirement of massively parallel HPC applications, which otherwise if ran on a DDR enabled platform will be very slow.
Another technology that I want to discuss is upcoming cheaper memories from Intel/Micron’s 3D XPoint memory. This technology has a promise of being much cheaper than DRAM/DDR but slower than DRAM, which raises the question is it possible to replace DRAM some of the DRAM capacity with this cheaper technology and not suffer and performance degradation.
So the problem that we need to solve is to exploit the difference in these memory technologies to match with different types of applications we want to run.
Verify above numbers
Remove LPDDR numbers
Leaving capacity for now

## Slide 6: Examples of heterogeneous systems
GPU
CPU
CPU-GPU Link
Unified Memory
DDR4
DDR4
DDR4
CPU
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
CPU memory
DDR technology
Graphics memory
GDDR/HBM technology
(higher bandwidth)
CPU
DDR4
DDR4
DDR4
Fast
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Slow
memory
Fast memory
DDR technology
Slow memory
3D XPoint technology
(cheaper but slower)
Coral system (IBM cpu, NVIDIA gpu)
https://www.olcf.ornl.gov/summit/
Two-tiered memory system
Notes: Now, lets look at two example heterogeneous memory systems that have different memory technologies built into a same system. First lets look at CPU-GPU platform that IBM and NVIDIA are building together for the next fastest supercomputer.

## Slide 7: Challenges
Match heterogeneous memories to application behavior
  Optimize for latency / bandwidth / programmability
Design and verification of multi-vendor systems
  “The single biggest problem in communication is the illusion it has already happened” – George Bernard Shaw
Increase perf/$ of large-scale system w/ increasing memory capacities
  Trend: applications with large in-memory datasets
Design application-transparent policies

## Slide 8: PhD research
2. Simplify CPU-GPU cache coherence implementation for programmability
3. Reduce memory cost in data-centers, while satisfying perf. targets
1. Maximize memory bandwidth for bandwidth-hungry GPU applications
“Page Placement Strategies for GPUs within Heterogeneous Memory Systems”, ASPLOS ’15
“Unlocking Bandwidth for GPUs in CC-NUMA systems”, HPCA ‘15
“Selective GPU Caches to Eliminate CPU-GPU HW Cache Coherence”, HPCA ’16
“Thermostat: Application-transparent Page Management for Two-Tiered Main Memory”, ASPLOS ‘17

## Slide 9: Outline
- Covered in Proposal
Bandwidth-asymmetric systems
  Policies maximizing memory bandwidth for GPGPU applications
Selective GPU caching
  Simplify CPU-GPU cache coherence implementation
Cheaper memory technologies
  A case for deploying cheaper but slower memories to increase perf/$
Notes: animate proposal

## Slide 10: CPU-GPU heterogeneous systems
CPU-GPU Link
Unified Memory
CPU
DDR4
DDR4
DDR4
CPU
memory
GPU
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
CPU memory
DDR technology
Graphics memory
GDDR/HBM technology
(higher bandwidth)
Coral system (IBM cpu, NVIDIA gpu)
What is new with CPU-GPU heterogeneous systems?
GPU can access CPU memory at much higher BW & lower latency
CPU-GPU Link
Conventional: PCIe
Higher latency (1-10us)
Lower bandwidth (~16GB/s)
All GPU data is placed in graphics memory
Upcoming: NVLink
Lower latency (~100ns)
Higher bandwidth (80GB/s)
Notes: NVLink is cache coherent
R1, R2, R3?

## Slide 11: Why do GPUs care about bandwidth?
Chart: Memory Bandwidth (GB/sec)
| 25.0 | 50.0 | 100.0 | 200.0 | 400.0 | 600.0
Average across General Purpose GPU apps | 0.42988 | 0.57464 | 0.76969 | 1 | 1.2532 | 1.3671
GPGPU apps are bandwidth-sensitive and latency-tolerant
Chart: Memory Latency (GPU cycles)
| 1.0 | 20.0 | 40.0 | 60.0 | 80.0 | 100.0 | 120.0 | 140.0 | 160.0 | 180.0 | 200.0
Average across General Purpose GPU apps | 1.0279 | 1.0229 | 1.0205 | 1.0109 | 1.0066 | 1 | 0.99534 | 0.98973 | 0.98338 | 0.97552 | 0.97157
Baseline
Better
CPU-GPU Link
CPU
DDR4
DDR4
DDR4
CPU
memory
GPU
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Unified Memory
Graphics memory
GPU data
CPU-GPU Link
CPU
DDR4
DDR4
DDR4
CPU
memory
GPU
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Unified Memory
Graphics memory
Future

## Slide 12: Existing data placement policies
Non-uniform memory access (NUMA) policies in OS [numactl]
  Local placement: optimize for lowering data access latency
  Interleave placement: distributes data equally among memory nodes
OS doesn’t have bandwidth differential information
  For example: difference in BW of CPU and graphics memory (2x-8x)
Due to lack of information, OS cannot place data efficiently
Notes: where existing? MAYBE CITATIONS

## Slide 13: Contribution: BW-AWARE placement
Chart: Throughput Normalized
| Local placement | Interleave placement | BW-AWARE placement
Average across General Purpose GPU Applications | 1 | 0.89286 | 1.1964
Place data in the ratio of the memory bandwidths
  Utilize bandwidth of all the available memory zones
BW-AWARE placement maximizes BW hence the GPU throughput
Better
GPU
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
CPU
DDR4
DDR4
DDR4
CPU
memory
BW: 1x
BW: 1x
BW: 2.5x
Average across General Purpose GPU Apps
[Agarwal ASPLOS’15]
Interleave
BW-AWARE
Local
100%
50%
50%
30%
70%
Notes: The main contribution of this work is how we implement this idea by correlating

## Slide 14: Contribution: BW-AWARE placement
Chart: Throughput Normalized
| Local placement | Interleave placement | BW-AWARE placement
Average across General Purpose GPU Applications | 1 | 0.89286 | 1.1964
Place data in the ratio of the memory bandwidths
  Utilize bandwidth of all the available memory zones
BW-AWARE placement maximizes BW hence the GPU throughput
Better
Average across General Purpose GPU Apps
Data in CPU memory | Data in Graphics memory | Policy
0 | 100% | Local
50% | 50% | Interleave
30% | 70% | BW-AWARE
[Agarwal ASPLOS’15]
GPU
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
CPU
DDR4
DDR4
DDR4
CPU
memory
BW: 1x
BW: 1x
BW: 2.5x

## Slide 15: Outline
- Covered in Proposal
Bandwidth-asymmetric systems
  Policies maximizing memory bandwidth for GPGPU applications
Selective GPU Caching
  Simplify CPU-GPU cache coherence implementation
Cheaper memory technologies
  A case for deploying cheaper but slower memories to increase perf/$
Notes: animate proposal

## Slide 16: Cache coherence in CPU-GPU systems
CPUs support HW cache coherence, why not CPU-GPU systems?
Pros:
  + Improves system programmability thus programmer productivity
  + Improves performance by fine-grained GPU access to CPU memory
Cons:
  Hard to design: merging different coherence protocols explodes state space
  Hard to implement and verify, especially in a multi-vendor setup
Can we provide illusion of a cache-coherent CPU-GPU system?
Notes: It’s well known that CPUs support cache coherence for making sure that shared data across different cores have either a single writer or multiple readers but not both simultaneously. It makes multi-core systems easier to program. In contrast, GPUs that were designed for graphics application acceleration do not support cache coherence as graphics applications do not have shared data. However, with wider adoption of GPUs for general purpose applications the question we need to revisit is the support for cache coherence. CPU designs have proven that cache coherence is highly desirable for programmability, however, supporting cache coherence in HW for a CPU-GPU heterogeneous system seems lucrative from programmers perspective can be really hard from designers point of view. Not only it is hard to to merge 2 different coherence domains, moreover the design and verification of a multi-vendor systems becomes extremely challenging when it comes to designing CPU-GPU HW cache coherence.

## Slide 17: Contribution: Selective GPU Caching
Chart: Throughput Normalized
| Local Placement | BW-AWARE w/ HW Cache Coherence | BW-AWARE w/ Selective GPU Caching
 | 1 | 1.2 | 1.116
Principle: GPU caches only if CPU is not caching, GPU is latency tolerant
Micro-architectural components to capture spatial/temporal locality
Average across General Purpose GPU Application
Better
HW cache coherence
✔Higher Performance
❌Higher design complexity
Selective GPU caching
✔ Higher performance
✔ Lower design complexity
[Agarwal HCPA’16]
CPU and GPU need not implement same cache coherence protocol

## Slide 18: Outline
- Covered in Proposal
Bandwidth-asymmetric systems
  Policies maximizing memory bandwidth for GPGPU applications
Selective GPU Caching
  Simplify CPU-GPU cache coherence implementation
Cheaper memory technologies
  A case for deploying cheaper but slower memories to increase perf/$
Notes: animate proposal

## Slide 19: Trends of data-center/cloud apps
Map datasets in memory
  Reduces data access latency ➤ performance benefit
  Reduces CPU time to run app ➤ lower cost
Increased memory installed / machine
  Memory is expensive, 30% of the machine cost
  3-10% of the data-center total cost of ownership
Goal: Increase performance per unit cost

## Slide 20: High-memory instances in cloud
Online accessed: Feb 12, 2017
2x-10x more expensive than standard instance

## Slide 21: Cheaper memory technologies
CPU
DDR4
DDR4
DDR4
DDR
50-100ns
Memory Technology | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
3D XPoint (expected) | 5x-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
Notes: Both the frequently accessed data, let’s call it hot and infrequently accessed data, let’s call it cold is mapped in DRAM.

## Slide 22: Cheaper memory technologies
hot data (frequently accessed)
cold data (infrequently accessed)
CPU
DDR4
DDR4
DDR4
DDR
50-100ns
Future
CPU
DDR4
DDR
XPoint
10x slower than DDR
50-100ns
Fast memory
Cheaper/slower memory
Mapping cold data to slow memory will free DRAM for other apps
Memory Technology ↓ | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
3D XPoint (expected) | 5x-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
Notes: Animation not that clear
However, with cheaper slower memory we can leverage the difference between data access frequency and place hot pages in fast DRAM and cold pages in cheaper/slower memory. Thus, there is an opportunity to cut down the DRAM requirement per application. Note that we only want to place those pages in slow memory that will not degrade application performance leading to SLA violations.

## Slide 23: How much slowdown is tolerable?
Trade-off:
Perf loss from slow memory vs. more machines for same perf
CPU
DDR
XPoint
CPU
DDR4
DDR4
DDR4
DDR
50-100ns
Savings = 30% *
XPoint
$(
)
Tight slowdown budget, we configure tolerable slowdown to 3%
To make up for perf. loss
+
CPU
DDR4
DDR
10x slower than DDR
50-100ns
Fast memory
Cheaper/slower memory
XPoint
CPU
DDR
XPoint
CPU
DDR
XPoint
✕
Notes: Explain the trade-off in machine cost/memory cost/performance

## Slide 24: Existing proposals: 2-tier memory
Application guided two-tier memory [Dullor EuroSys’16]
SW-managed two-tier memory [Lim HPCA’12, AutoNUMA]
HW-managed two-tier memory [Ekman IPDPS’05, Qureshi MICRO’09, Sim MICRO’12, Jevdjic MICRO’14]
Not governed by application performance requirements
No support for huge pages
Notes: Why huge pages break their solution:
Whether we have hot cold huge pages, no one has even asked that question
whether method for classification: low overhead
  Profiling technique to identify data to be placed in slow memory
  On-demand page migration from slow to fast memory
  DRAM as a cache, invisible to OS

## Slide 25: Why huge pages?
u Fewer TLB misses
TLB
Application working set
mapped on small pages
0
4KB
8KB
12KB
16KB
Reachable by TLB
Out of TLB reach
...
8MB
Application working set
mapped on huge pages
0
2MB
4MB
Reachable by TLB
8MB
Small page: 4KB
Huge page: 2MB
Notes: What is the huge and why?
First, they lead to fewer TLB misses as they are able to cover larger fraction of memory by a single TLB entry. A system with 4 TLB entries if managed at 4KB granularity can reach only 16KB of footprint without any TLB misses.

## Slide 26: Huge pages – Advantages
u Fewer TLB misses
Faster TLB misses
  3 instead of 4 level tree lookup
  Better cacheability of PTEs
Performance benefit up to 30% under virtualization
Cloud platforms benefit significantly
  Virtualization page walks:
  24 (4KB) ➤ 16 (2MB)
Notes: super critical for clloud
Second advantage of 2MB pages is that they make every TLB miss faster. Instead of doing a 4-level tree lookup, page walk needs to be only done on a 3-level tree, which also reduces the pressure on data caches.
Merge this slide with previous
The main difference between our work and prior work in 2-tier memory systems is support for huge pages. Here I show you why huge pages are important from performance perspective.
Explain graph
1.x

## Slide 27: Problems to solve
Low-overhead cold page detection mechanism
  Very tight performance slowdown budget
Support for huge pages
  Huge pages are critical to application performance
Application-transparent mechanism
  Source code of cloud applications may not be available
Thermostat: Places up to 50% of application footprint in cheaper/slower memory while satisfying 3% tolerable slowdown
[Agarwal ASPLOS’17]
Notes: Low overhead mechanism that identifies cold data at runtime
Application transparent manner
while supporting huge pages
while satisfying perf. requirements
I will present my solution to this problem that we call Thermostat, which we prototyped in Linux 4.5

## Slide 28: Cold data ➤ slow memory
Time
0s
1s
1.03s
Extra time per sec
1us/access
3% slowdown in app ⇒ 30K accesses/sec from slow memory of 1us latency
Pages below 30K cumulative accesses/second are “cold”
…
30,000 accesses
Notes: COMA and many of the ideas that came to fruition in the 90's in the context of shared memory machines. COMA machines and even optimized CC-NUMA machines (e.g., Excel-NUMA) were exploring capacity and latency trade offs in multiple block-based cache hierarchy levels. You may find ideas that were developed and even built in machines (e.g., KSR and Sun WildFire/Reactive NUMA) of importance and inspiration. All of these address multi-level cache/DRAM hierarchies.

## Slide 29: Existing proposals: Accessed bit based
Physical address Accessed bit ...
A 1
B 1
E 0
...
S 0
...
Intel x86 page table entries (simplified)
A
B
C
D
TLB
u Accesses page E
TLB miss
1
Hardware has single “Accessed” bit per page
v
w HW page walk
x
1
1
E
y
Based on HW “accessed” bit
Used for working set estimation [Waldspurger OSDI‘02][Lespinasse ‘11][Guo VEE’15]
Tracking page access rate [Zhou ASPLOS’04]
“Accessed” bit is read and cleared, and TLB flushed at fixed intervals
Notes: Transition from Thermostat to Accessed bit not clear
TODO: Color code PTEs as well

## Slide 30: Issue with HW ‘Accessed’ bit
HW “Accessed” bit/page is not a good indicator of page access rate
Trade-off: cold page detection accuracy vs. performance slowdown
Redis
Each dot represents a 2MB page
Scan interval 10 sec
Chart: Scan interval for "Accessed" bit (sec)
| 1.0 | 2.0 | 5.0 | 7.0 | 10.0 | 20.0
Redis | 31 | 23 | 10 | 4 | 0.95 | 0.94
Better
Tolerable slowdown 3%
Notes: Why accessed bit: not work in our envronment
Experiment: overhead vs accuracy

## Slide 31: Thermostat detection
Estimate page access rate using s/w induced fault mechanism
  Cold page detection overhead (< 1%)
Tolerable slowdown governed use of slow memory
  Move cold pages to slow memory controlling slow mem. access rate
  Input parameter: slowdown application can tolerate
1. Page sampling
2. Page classification
3. Phase change detection

## Slide 32: Page sampling
...
2M
2M
2M
Application huge pages

## Slide 33: Page sampling
...
2M
2M
2M
Application huge pages
Sampled
Continuously sample a random fraction of huge pages

## Slide 34: Page sampling
...
2M
2M
2M
4K
...
4K
4K
4K
4K
Split
Application huge pages
Sampled
Continuously sample a random fraction of huge pages
Split the sampled huge page into 4KB pages

## Slide 35: Page sampling
...
2M
2M
2M
4K
...
4K
4K
4K
4K
Split
Application huge pages
Sampled
Accessed
Continuously sample a random fraction of huge pages
Split the sampled huge page into 4KB pages
Only sample 4K pages for which hardware Accessed bit is set

## Slide 36: Page sampling
...
2M
2M
2M
4K
...
4K
4K
4K
4K
4K
...
4K
4K
4K
4K
Split
Poison
4K
Application huge pages
Sampled
Accessed
Poisoned
Continuously sample a random fraction of huge pages
Split the sampled huge page into 4KB pages
Only sample 4K pages for which hardware “Accessed” bit is set
Record accesses to a few 4KB pages using s/w induced fault

## Slide 37: Page sampling
...
2M
2M
2M
4K
...
4K
4K
4K
4K
4K
...
4K
4K
4K
4K
Split
Poison
4K
Application huge pages
Sampled
Accessed
Poisoned
Merge
2M
Continuously sample a random fraction of huge pages
Split the sampled huge page into 4KB pages
Only sample 4K pages for which hardware Accessed bit is set
Record accesses to a few 4KB pages using s/w induced fault
Merge the split page back to huge page

## Slide 38: Page classification
For tolerable slowdown 3%, 1us slow memory latency, slow mem access rate = 3%/1us = 30k/sec
Pages in Slow Mem
Pages in DRAM
2M
2M
2M
...

## Slide 39: Page classification
For tolerable slowdown 3%, 1us slow memory latency, slow mem access rate = 3%/1us = 30k/sec
Estimate huge page access rate by poisoned 4K pages
Pages in Slow Mem
Pages in DRAM
...
2M
2M
Sort by access frequency
2M

## Slide 40: Page classification
For tolerable slowdown 3%, 1us slow memory latency, slow mem access rate = 3%/1us = 30k/sec
Estimate huge page access rate by poisoned 4K pages
Pages in Slow Mem
Pages in DRAM
...
2M
2M
Sort by access frequency
2M
30k/sec,
scaled by sampling fraction
Migrate to slow mem

## Slide 41: Phase change detection
Pages behavior may change over time
Measure access rate to all cold pages & sort by access frequency
Pages above 30K total access rate get migrated back to DRAM
Pages in Slow Mem
Pages in DRAM
...
2M
2M
2M
2M
Sort by access frequency
2M
...

## Slide 42: Phase change detection
Pages behavior may change over time
Measure access rate to all cold pages & sort by access frequency
Pages above 30K total access rate get migrated back to DRAM
Pages in Slow Mem
Pages in DRAM
...
2M
2M
2M
2M
Sort by access frequency
2M
30k/sec
...
Migrate back to DRAM

## Slide 43: Thermostat: example
Thermostat continuously samples pages to detect cold data at runtime

## Slide 44: Page access counting
SW based page poisoning to induce fake faults: ~1us
TLB misses correlates with LLC misses for cold pages

## Slide 45: Page access counting
SW based page poisoning to induce fake faults: ~1us
TLB misses correlates with LLC misses for cold pages
A
TLB
poison bit
B
C
D
Page table entries
A
B
C
D
0
0
1
0
E
1
...
...

## Slide 46: Page access counting
SW based page poisoning to induce fake faults: ~1us
TLB misses correlates with LLC misses for cold pages
TLB
poison bit
Page table entries
Application access page E
A
B
C
D
TLB miss
A
B
C
D
0
0
1
0
E
1
...
...

## Slide 47: Page access counting
SW based page poisoning to induce fake faults: ~1us
TLB misses correlates with LLC misses for cold pages
TLB
poison bit
Page table entries
Application access page E
1
Fake fault handler:
1. Un-poison PTE
A
B
C
D
TLB miss
A
B
C
D
0
0
1
0
E
0
...
...

## Slide 48: Page access counting
SW based page poisoning to induce fake faults: ~1us
TLB misses correlates with LLC misses for cold pages
TLB
poison bit
Page table entries
Application access page E
1
Fake fault handler:
1. Un-poison PTE
2. Install TLB entry
2
A
E
C
D
TLB miss
A
B
C
D
0
0
1
0
E
0
...
...

## Slide 49: Page access counting
SW based page poisoning to induce fake faults: ~1us
TLB misses correlates with LLC misses for cold pages
TLB
poison bit
Page table entries
Application access page E
3
Fake fault handler:
1. Un-poison PTE
2. Install TLB entry
3. Re-poison PTE
2
A
E
C
D
TLB miss
A
B
C
D
0
0
1
0
E
1
...
...
BadgerTrap [Gandhi CAN’14]

## Slide 50: Evaluation platform
72-core (HT), Intel Xeon E5-2699 v3, prototype in Linux 4.5
Control groups: resource isolation of client and server threads
Split randomly selected 5% pages, scan period = 10 seconds
Socket-1
Application-server
inside VM
(kvm, 8 cores)
256 GB
Socket-2
Client /
Load generator
256 GB
QPI
CPU
CPU

## Slide 51: Applications
TPC-C on MySQL
Online transaction processing (OLTP) benchmark
Fulfill customer orders to supply products from a company, widely used app
5 transaction (new-order + payment ~ 85%), write-intensive, file I/O heavy
Cassandra
NoSQL database, wide-column with variable number of fields per key
Netflix is one of the biggest users, AppScale, Wikimedia, Apple, and any more
File I/O heavy, compacts its SSTables data structure on disk
Redis
NoSQL based single-threaded key-value store, in-memory database
Github, Twitter, Pinterest, Snapchat, and many more users

## Slide 52: MySQL-TPCC
Dominated by write transactions
  New order + payment: ~85%
Largest table in schema: LINEITEM
  Read infrequently ⇒ cold data
  Cold data from file cache
50% data in slow memory, 1.3% throughput degradation

## Slide 53: Cassandra
Data stored in immutable SSTables
  Cached as memtables in memory
  SSTables grow with writes
  Compacted at a fixed frequency
  Read requests served by memtables
  SSTables not accessed frequently
  SSTables ⇒ cold data
30-50% data in slow memory, 2% throughput degradation

## Slide 54: Redis
15% data in slow memory, 2% throughput degradation
In-memory key-value store
  Large hash table
  Keys distributed uniformly per page
High-throughput database
  Cold data detected is low

## Slide 55: Sensitivity to slowdown parameter
Fraction of cold data increases with higher tolerable slowdown
Chart: Specified tolerable slowdown (%)
| 3.0 | 6.0 | 10.0
Cassandra | 45 | 54 | 60
MySQL-TPCC | 50 | 57 | 61
Redis | 10 | 25 | 32

## Slide 56: Summary: Thermostat
Manages huge pages in a two-tier memory system
Application-transparent, low overhead mechanism
Cost benefit of slow memory + perf benefit of huge pages
Prototyped in Linux 4.5
Places up to 50% data within 3% performance slowdown
Tolerable slowdown governed mechanism

## Slide 57: Thesis summary
CPU-GPU heterogeneous systems
  Application-transparent BW maximizing data management policies
    Improve GPU throughput, thus reduce application runtime
  Programmability with performance and design simplicity
    Provide illusion of HW cache coherence with a simplified design
A case for deploying cheaper/slower memories in cloud
  Cost benefit of slow memories + perf. of huge pages
[Agarwal ASPLOS’17]
[Agarwal ASPLOS’15, HPCA’15]
[Agarwal HPCA’16]

## Slide 60: Thesis committee

## Slide 61: Collaborators

## Slide 63: Load generator
Notes: load gen ?

## Slide 64: Migration & slow memory accesses
Data Transfer (MB/sec) | Migration | False-classification
Aerospike | 13.3 | 9.2
Cassandra | 3.8 | 3.8
In-mem-analytics | 16 | 0.4
MySQL-TPCC | 6 | 1.8
Redis | 11.3 | 10
Web-search | 1.6 | 0.3
Migration/false classification rates below expected BW of future memories
Notes: Give the expected number here?

## Slide 65: Paving a path for simplifying CPU-GPU coherence
Neha Agarwal
University of Michigan
Thomas Wenisch
David Nellans
Eiman Ebrahimi
John Danskin
Steve Keckler
Notes: Hi Everyone, I am Neha Agarwal from University of Michigan. And, today I am going to talk about my work on how can we simplify CPU-GPU cache coherence designs. I and my advisor Tom Wenisch did this work with our collaborators at NVIDIA. This work was pretty interesting as our focus was on simplifying the design as much as possible for making adoption of the idea in industry feasible.

## Slide 66: Discrete CPU-GPU systems
CPUs and GPUs connected via cache-line granularity interconnect
Is coherence support necessary over this link?
GPU
CPU
Dedicated CPU-GPU Link
Unified Memory
DDR4
DDR4
DDR4
CPU
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphicsmemory
Cache-line granularity link
(e.g., NVIDIA’s NVLINK)
Notes: CPU-GPU platforms have gained a lot of importance as of late, and multiple vendors are involved with building such systems
The most powerful GPUs today are built on a separate die due to thermal and die area constraints and have their own specialized memory systems. Moreover, such discrete CPU GPU systems come from different vendors precluding single-die integration
In the context of this work we’re focusing on such discrete CPUs and GPUs that are connected via a cache-line granularity dedicated CPU-GPU interconnect such as NVIDIA’s NVLINK
We are particularly interested in investigating whether it is necessary to support cache coherence over such a link?

## Slide 67: Why CPU-GPU cache coherence?
Improves programmer productivity by eliminating manual data copying
Improves performance via fine-grained access to remote memory
Goal: High performance coherent address space
GPU
CPU
Dedicated CPU-GPU Link
Unified Memory
DDR4
DDR4
DDR4
CPU
memory
Line
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphicsmemory
Page
Notes: In the context of these discrete CPU-GPU systems, introducing unified shared CPU-GPU memory has multiple potential benefits and is a concept being adopted by multiple vendors. Consider a system where all of memory, whether it is attached to the CPU or the GPU is treated as a unified globally visible address space and either the CPU or GPU can make requests to any part of this memory.
Now this notion of unified memory has gained traction because it improves programmer productivity by eliminating explicit copying of data and manual memory management. Traditionally, when there was an access for example from the GPU to a page that was in CPU-attached memory, that page
would need to copied over to graphics memory.
We further improve programmer productivity and system performance by allowing fine grained access from the GPU to the CPU memory.
Our goal with this work is to provide a high performance shared virtual address space -- irrespective of the consistency model being assumed
Now by making all the caches in this system HW cache coherent can solve this design problem, however,

## Slide 68: CPU-GPU HW cache coherence is DIFFICULT
1. Cache coherence state space explosion
Notes: Now here is an example state space diagram for 2 different CPU cache coherence protocols combined to support all the states in both of the protocols. As we can look, this horrifying diagram has many states for the combined protocol to work correctly. Now imagine combining such complex cache coherence protocols from a CPU vendor and a GPU vendor. Its not difficult to see that such a cache coherent design will have large number of states calling for huge design and verification effort from the engineers.

## Slide 69: CPU-GPU HW cache coherence is DIFFICULT
2. Vendor collaboration
Notes: Since these discrete CPU GPU systems come from different vendor another challenge for these vendors is to come up with a design together.
Collaborating across different teams within the same company can be quiet challenging, but its another can of worms when designs have to be made to work correctly across companies. So, given how complex cache coherence design can get, our goal with this work was to simplify the design itself, thus cut down on the verification challenge and deliver the product timely.

## Slide 70: Goal: Simplify CPU-GPU coherence design
1. Cache coherence state space explosion
Restrict GPU’s caching ability exploiting GPU’s latency tolerance
2. Vendor collaboration
CPU and GPU need not implement same coherence protocol
Solution: Selective GPU caching
Notes: To address the problem of state space explosion our key idea is to restrict the GPU’s ability to cache data and exploit the GPU’s latency tolerance properties to have minimal effect on performance
And to address the challenge of vendor collaboration we want a solution that doesn't require CPU and GPU to implement same cache coherence protocol.
Our solution to address above challenges is Selective GPU caching with which we provide globally visible shared memory w/o HW cache coherence

## Slide 71: Selective GPU Caching: Principles
CPU caching capability remains intact
GPU doesn’t need to handle coherence traffic from CPU
1. CPU caches both CPU- & graphics-memory
2. GPU never caches CPU-memory
3. GPU caches graphics-memory
if CPU not caching
Directory
CPU
Remote Directory
DDR4
DDR4
DDR4
CPU
memory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Graphics
memory
GPU
Notes: Selective caching is based on these three principles:
CPU caches all of memory, the GPU never caches the CPU attached memory, and the GPU only caches GPU-memory only if CPU is not caching it.
Envision a simple system such as the one shown here. We’ve got one CPU and one GPU with DDR connected to the CPU, GDDR connected to the GPU and a dedicated link connecting the two…
The primary micro architectural structure needed to implement selective caching is a remote directory on the GPU side. This directory approximately but conservatively tracks the lines homed in GPU memory that are presently cached at the CPU.
Now if the GPU reads from an address mapped to DDR memory on the CPU side, the regular directory sends the most recent copy. If the GPU writes to DDR memory, the directory handles invalidation of CPU side caches. If the CPU reads/writes GDDR, then the line is inserted in the remote directory. The GPU uses this filter to figure out whether or not it can cache a given line. If a line is found in the filter, the GPU can’t cache it.
What I just described is a pretty primitive and naïve implementation of selective caching. We expect this level of naively bypassing GPU caches to result in some loss of performance compared to a fully cached solution.

## Slide 72: Performance vs Design complexity trade-off
Uses link bandwidth inefficiently
Uses remote DRAM bandwidth
inefficiently
Misses out on bandwidth savings
from caching locality
Chart: Performance Relative to HW Cache Coherence
| backprop | bfs | btree | CNS | CoMD | kmeans | MiniFE | mummergpu | needle | pathfinder | srad_v1 | XSBench | GMEAN
Naive Selective Caching | 0.43797 | 0.59005 | 0.09489 | 0.2696 | 0.16299 | 0.94807 | 0.44781 | 0.40564 | 0.88174 | 0.6062 | 0.91293 | 0.32449 | 0.41912
HW cache coherence
✔High Performance
❌High design complexity
Selective GPU caching
❌ Low performance
✔ Low design complexity
How can we make Selective GPU Caching high performant?
Notes: This graph shows the performance effect of a naïve implementation of selective caching as we described it on the previous slide normalized to a base line that has fully coherent CPU and GPU caches for different applications.
This graph shows that this loss of performance is on average greater than 50% and
Sometimes as large as 80-90% in the case of applications like btree and comd. To bridge this performance gap we came up with some micro architectural enhancements.

## Slide 73: Performance enhancements to Selective Caching
1. Aggressive Request Coalescing
2. CPU-side client cache
3. Variable-size link transfers
Reduces CPU memory traffic from the GPU
Spatially coalesces GPU requests to CPU memory
Directory
CPUs
Client Cache
Request Coalescer
DDR4
DDR4
DDR4
CPU
memory
GPU
Variable-size Transfer
Improves CPU-GPU interconnect efficiency
u
w
v
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Graphicsmemory
Notes: Here are three optimizations we have developed. I’ll go over each optimization and how it closes the gap in performance I just showed.

## Slide 74: Performance enhancements to Selective Caching
1. Aggressive Request Coalescing
2. CPU-side client cache
3. Variable-size link transfers
Reduces CPU memory traffic from the GPU
Spatially coalesces GPU requests to CPU memory
Directory
CPUs
Client Cache
Request Coalescer
DDR4
DDR4
DDR4
CPU
memory
GPU
Variable-size Transfer
Improves CPU-GPU interconnect efficiency
u
w
v
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Graphicsmemory
Notes: The first is to implement aggressive MSHR request coalescing for requests sent to CPU memory.

## Slide 75: Request Coalescing: Captures spatial locality
16B req
GPU
CPU
DDR4
DDR4
DDR4
CPU
memory
1
16B req
16B req
1
16B req
1
128B data
16B data
16B data
16B data
Miss Status Holding Register (MSHR)
16B data
16B data
16B data
16B data
16B data
16B req
16B req
16B req
16B req
16B req
16B req
16B req
128B req
35% requests are coalesced≈ 80% of L1-hits
Notes: With request coalescing we want to Reduce the number of requests made to CPU-memory from the GPU
We use miss status holding registers in GPU to track outstanding cache misses, however, remember we will not cache any data returned from the CPU memory.
For the sake of this example I’ll assume 16B requests showing up from the GPU.
To do this, we promote the granularity of individual load requests before issuing them to the DDR memory system. This means an individual load request, is promoted to 128B or the size of a cachline before being issued as a request
While this larger request is in flight, if other requests are made within the same 128B block, then these requests can simply be attached to the pending request list in the corresponding MSHR and no new requests are issued to the memory system.
Now to maintain correctness in a non-caching system any parts of the returning 128B block that haven’t been requested are going to be discarded immediately on arrival to the GPU.
It turns out there a good deal of spatial locality that can be captured this way. On average 35% of memory requests can be serviced via cacheless request coalescing. While this may seem like a low absolute number, we are capturing spatial locality and providing the majority of the benefit of L1 caches with a much lower overhead approach of simply coalescing at the MSHRs.

## Slide 76: Request Coalescing: Performance
20%
Notes: This graph shows how request coalescing affect performance compared to a naïve selective caching solution.
The request coalescing referred to as L1-L2 request coalescing simply means that its happening at both L1 and L2 cache levels.
We find that we can close the gap to within 20% the performance of full caching just by adding this first optimization on top of the described naïve selective caching implementation. However, although request coalescing exploits spatial locality, it does not capture temporal locality and there are other inefficiencies that we aim to address.

## Slide 77: Performance enhancements to Selective Caching
1. Aggressive Request Coalescing
2. CPU-side client cache
3. Variable-size link transfers
Reduces CPU memory traffic from the GPU
Spatially coalesces GPU requests to CPU memory
Directory
CPUs
Client Cache
Request Coalescer
DDR4
DDR4
DDR4
CPU
memory
GPU
Variable-size Transfer
Improves CPU-GPU interconnect efficiency
u
w
v
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Graphicsmemory
Notes: If request coalescing fails to capture re-use of a cache line, then over time multiple requests for the same line in CPU memory may be sent to the memory controller causing inefficiency in utilizing DDR by the GPU. To address this inefficiency, the second optimization we developed is a CPU-side GPU client cache.

## Slide 78: CPU-side Client Cache: Capture temporal locality
Prevent requests for the same line in CPU-memory
Participate in CPU coherence protocol
Only allocate lines upon request of the GPU
GPU
CPU
DDR4
DDR4
DDR4
CPU
memory
Client Cache
GPU Req
GPU Data
GPU Req
GPU Data
GPU Data
Coherence traffic within CPU die only
Notes: The key idea of this CPU side client cache is to shield the DDR memory system from repeated requests for the same line when request coalescing does not capture temporal reuse
This cache participates in the CPU coherence protocol like any other coherent cache on the CPU die
This single new cache does not introduce the coherence and interconnect scaling challenges of the GPU side caches while still providing latency and bandwidth filtering advantages for GPU requests.
Explain the animation.
This client cache thus captures temporal locality from the traffic generated by the GPU.
Note that this cache only allocates lines upon request by an off-chip processor such as the GPU. We put this client cache on the CPU side in order to not bring any coherency onto the GPU die.

## Slide 79: CPU-side Client Cache: Performance
10%
Notes: This graph shows the performance impact of adding the CPU side client cache on top of the request coalescing described earlier. Here we show performance for client side of 256KB to 1MB. The performance improvements scale up with the size of this cache up till around a 512KB cache and then start to taper off. Combining such a 512KB 8-way associative client cache with request coalescing gets us to within 10% of the performance of a fully HW cache coherent CPU-GPU solution.

## Slide 80: Performance enhancements to Selective Caching
1. Aggressive Request Coalescing
2. CPU-side client cache
3. Variable-size link transfers
Reduces CPU memory traffic from the GPU
Spatially coalesces GPU requests to CPU memory
Directory
CPUs
Client Cache
Request Coalescer
DDR4
DDR4
DDR4
CPU
memory
GPU
Variable-size Transfer
Improves CPU-GPU interconnect efficiency
u
w
v
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Graphicsmemory
Notes: Our third optimization is variable-size link transfers over CPU GPU interconnect.

## Slide 81: Data over-fetch across CPU-GPU interconnect
16B req
GPU
CPU
DDR4
DDR4
DDR4
CPU
memory
1
16B req
16B req
1
16B req
1
128B data
16B data
16B data
16B data
Miss Status Holding Register (MSHR)
16B data
16B data
16B data
16B data
16B data
16B req
16B req
16B req
16B req
16B req
16B req
16B req
128B req
40% of data is discarded without being consumed
Notes: An average cacheline utilization of 60% indicates that just 77 out of 128 bytes transferred are actually used by the GPU.
So 40% of transferred bytes are immediately discarded without even being consumed.
We reduce the transfer unit from 128B down to 64B or 32B to improve the bandwidth utilization of CPU-GPU interconenct.
But then we need to deal with trade-offs associated with packetization overheads. If the data transfer unit is smaller then fixed size packet overhead can reduce the overall link utilization. For example, with 16B packet headers, if we fetch all data in 128B cache line then the link utilization is 88%, however link utilization reduces to 66% in case of 32B data transfer units.
So to maintain the benefit of request coalescing but reduce interconnect inefficiency we use variable transfer units on the CPU-GPU interconnect.

## Slide 82: Variable size link transfers: Key Ideas
16B req
GPU
CPU
DDR4
DDR4
DDR4
CPU
memory
1
16B req
16B req
1
16B req
1
128B data
Miss Status Holding Register (MSHR)
16B req
16B req
16B req
16B req
16B req
16B req
16B req
128B req
1
1
1
16B data
16B data
16B data
Notes: To enable the variable size link transfers, we embed a bit-mask in each request header indicating which sub-blocks of the 128B cache line should be transferred back. The
What happens here is that while an initial request is pending across the CPU-GPU interconnect, we merge any further sub-blocks with whatever the initial bit-mask indicated
  Its worth noting here that variable size transfer units are also understood by the MSHRs of the CPU-side client cache that we talked about in the second optimization …By maintaining this mask when CPU memory returns a 128B cache line only the requested sub-blocks are returned to the GPU

## Slide 83: Variable size link transfer: Impact on traffic
Notes: This graph shows the impact of variable size transfer on the data transferred across the CPU-GPU interconnect.
For each benchmark the bars show relative transfer of data across the interconnect, you can see a significant drop on the amount of data transferred using the variable size transfer technique.
The big gain with this optimization is the significantly less amount of data transferred across the link which can enables power savings. Performance (which we don’t show in this graph) significantly improves for some benchmarks but on average the improvement is relatively smaller than the previous enhancements and we see a 3% performance improvement from this optimization.

## Slide 84: Conclusion: Selective Caching
CPUs and GPUs do not need to be HW cache coherent to achieve the benefits of unified memory and high GPU performance
With request coalescing, a CPU-Side GPU client cache, and variable sized link transfer, we come within 7% of a HW cache coherent GPU
Promiscuous read-only caching benefits latency-sensitive applications using OS-page protection mechanisms

## Slide 85: Selective GPU caching with HW changes
Chart: Performance wrt HW Cache Coherence
| Naive Selective Caching | L1L2-MSHR Coalescing | 512KB-Client Cache | Variable size transfers
 | 0.42 | 0.799 | 0.8977 | 0.927
7%
Notes: Pulling the results from all the optimizations together, this is what the summary looks like
If we normalize everything to a fully coherent solution
We see that a naïve selective caching solution loses a lot of performance
But adding the aggressive MSHR coalescing, the client cache, and variable transfer units get us to within 7% of a fully coherent system.

## Slide 86: Does GPU have to avoid caching CPU memory?
60% of data is read-only
GPU could cache such read-only data safely
Notes: Up until this point, I’ve described three mechanisms which are basically hardware optimizations and, they all assume the GPU strictly never caches any part of CPU memory. The question is, does the GPU have to avoid caching CPU memory all the time?
This graph shows the fraction of data touched by the GPU that is read only vs both read and written at an OS page granularity. We find that in many workloads the majority of data touched by the GPU is read-only at an OS page level.
In fact, 60% of the data is read-only. The idea here is that the GPU could potentially cache such read-only data safely, and we could guarantee correctness through OS page protection mechanisms entirely in software.

## Slide 87: Promiscuous Read-only Caching: SW mechanism
Predict read-only pages
and allow GPU to cache them
Use software fault handler
to clean up mispredictions
Effectiveness determined by
prediction accuracy and miss-prediction penalty
Chart: Performance wrt HW Cache Coherence
| HW Selective Caching | +Read-Only (20us) | +Read-Only (30us) | +Read-Only (40us)
 | 0.927 | 1.02 | 1.01 | 0.999
Notes: To this end, we investigate and propose promiscuous read only-caching. In this mechanism, both the CPU and the GPU can cache all of CPU memory with read-only page protection bits in page tables to guarantee correctness. Essentially, on a read to a page a prediction is made as to whether it’s a read-only page. If a write comes to such a page, a protection fault is raised, upon which the software fault handler flushes the corresponding lines from the GPU caches, and the write bit is set on the page table entry. The GPU inspects the page protection of each page before caching it, and if it is in a read-write state, does not cache it. This software mechanism ensures that coherence is maintained, while not penalizing caching accesses to read-only lines.
In the graph on the right, we can see that read-only caching performs at-par with hardware cache coherence.
Some workloads exhausting the GPUs ability to overlap execution with the faults. Hence, suffer considerable slowdowns due to exposed protection fault latency. For such workloads we can disable promiscuous read-only caching in the software. Nevertheless, this mechanism can gain performance by effectively caching a large fraction of read-only data present in many other GPU applications.

## Slide 88: HW Selective Caching – all workloads
Chart: Performance Relative to HW Cache Coherence
| backprop | bfs | btree | CNS | CoMD | kmeans | MiniFE | mummergpu | needle | pathfinder | srad_v1 | XSBench | GMEAN
HW Coherence | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Naive Selective Caching | 0.43797 | 0.59005 | 0.09489 | 0.2696 | 0.16299 | 0.94807 | 0.44781 | 0.40564 | 0.88174 | 0.6062 | 0.91293 | 0.32449 | 0.41912
L1L2-MSHR-coalescing | 0.9421 | 0.88765 | 0.53509 | 0.56257 | 0.62932 | 0.94689 | 0.84149 | 0.94596 | 0.89491 | 0.99949 | 1.0546 | 0.55703 | 0.79396
512KB MC-Cache | 0.99591 | 1.0011 | 0.5639 | 0.75034 | 0.70528 | 1.0239 | 0.93742 | 1.0028 | 0.92952 | 0.99934 | 1.0645 | 0.96752 | 0.89772
Variable Transfer | 0.99944 | 1.0018 | 0.56395 | 0.83108 | 0.90348 | 1.0281 | 0.96593 | 0.99405 | 0.92882 | 0.99943 | 1.0645 | 0.97611 | 0.9272
7%
Notes: Pulling the results from all the optimizations together, this is what the summary looks like
If we normalize everything to a fully coherent solution
We see that a naïve selective caching solution loses a lot of performance
But adding the aggressive MSHR coalescing, the client cache, and variable transfer units get us to within 7% of a fully coherent system.

## Slide 89: Promiscuous Read-only Caching
Predict read-only pages
and allow GPU to cache them
Use software fault handler
to clean up mispredictions
Effectiveness determined by
prediction accuracy and miss-prediction penalty
Notes: To this end, we investigate and propose promiscuous read only-caching. In this mechanism, both the CPU and the GPU can cache all of CPU memory with read-only page protection bits in page tables to guarantee correctness. Essentially, on a read to a page a prediction is made as to whether it’s a read-only page. If a write comes to such a page, a protection fault is raised, upon which the software fault handler flushes the corresponding lines from the GPU caches, and the write bit is set on the page table entry. The GPU inspects the page protection of each page before caching it, and if it is in a read-write state, does not cache it. This software mechanism ensures that coherence is maintained, while not penalizing caching accesses to read-only lines.
In the graph on the right, we can see that read-only caching performs at-par with hardware cache coherence.
Workloads like backprop, cns, needle tend to issue many concurrent writes, exhausting the GPUs ability to overlap execution with the faults. Hence, suffer considerable slowdowns due to exposed protection fault latency. For such workloads we can disable promiscuous read-only caching in the software. Nevertheless, this mechanism can gain performance by effectively caching a large fraction of read-only data present in many other GPU applications.

## Slide 90: Data Over-fetch across CPU-GPU interconnect
Reduce transfer unit: 128B down to 64B or 32B?
Trade-offs with packetization overhead
We propose variable-size link transfers
Workload | Avg. Cacheline Utilization (%)
backprop | 86
bfs | 37
btree | 79
cns | 78
comd | 33
kmeans | 25
minife | 92
mummer | 46
needle | 39
pathfinder | 87
srad_v1 | 96
xsbench | 30
Average | 60
Notes: This table shows the amount of data over-fetch across our evaluated benchmarks. In this table cacheline utilization refers to the fraction of the transferred line that has a pending request when the GPU receives a cacheline-sized response from CPU memory. An average cacheline utilization of 60% indicates that just 77 out of 128 bytes transferred are actually used by the GPU.
So 40% of transferred bytes are immediately discarded
We might want to reduce the transfer unit from 128B down to 64B or 32B to improve this
But then we need to deal with trade-offs with packetization overheads. Assuming all data is used (which isn’t the case obviously), but if all the data in what is returned were used at 32B granularity we’d at best have 66% link utilization, but at 128B granularity we’d have 88% link utilization.
So to maintain the benefit of request coalescing but reduce interconnect inefficiency we propose using variable transfer units on the CPU-GPU interconnect.

## Slide 91: Problem!
20+
Cores
(CPU)
100+ SMs
(GPU)
20+
Cores
(CPU)
100+ SMs
(GPU)
Future: Hundreds of coherent caches?
CPU-GPU Link
CPU-GPU Link
Cache-coherent Link
Hard to implement in a timely manner
change diagram
Notes: The problem is…
But when we start adding GPUs, GPUs are expected to have up to hundreds of streaming SMs each with their own cache, trying to extend traditional cache coherency into the GPU memory system requires keeping hundreds of caches coherent. And its fairly well known that scaling cache coherence to this degree is pretty difficult and requires both very large state and very large interconnect bandwidth. This makes it fairly unattractive to build fully cache coherent systems using this approach.
This proves even more difficult with multiple vendors trying to integrate existing CPU and GPU designs in a timely manner.

## Slide 92: CPU-GPU heterogeneous systems
Simplifying CPU-GPU coherence [HPCA’16]
  CPU and GPU need not implement same cache coherence protocol
  Simplifies vendor collaboration

## Slide 93: Discrete CPU-GPUs
Simplifying CPU-GPU coherence [HPCA’16]
  CPU and GPU need not implement same cache coherence protocol
  Simplifies vendor collaboration
BW-aware page placement & migration [ASPLOS’15] [HPCA’15]
  Maximizes b/w available to GPU by optimal page placement
  Intelligent page prefetch when all data starts off in CPU memory

## Slide 94: Heterogeneous Memory Systems
Can be found everywhere

## Slide 95: Why build heterogeneous memory systems?
2 issues:
with variation in application patterns we cannot use one memory technology for all applications
  Talk about BW hungry GPU apps
  so, we have high bandwidth memories for GPUs
  but we also have CPU attached memory
  so, what is the optimal way to utilize both of these memory zones
Memory capacity / machine increasing, but memory is expensive (30% of machine cost), lots of money, memory management of increased memory size/machine is challenging
Match memory access patterns, reduce CPU time, save cost

## Slide 96: Cold data in applications with huge pages
Mechanisms built on ‘accessed’ bit cannot provide perf. guarantees
Detection by scanning hardware ‘Accessed’ bit in PTE at 10s interval
Notes: But if we start detecting cold pages at 2MB granularity the amount of cold data detected is much less. It’s because of the way current OS level cold page detection mechanisms work. They only operate at page granularity. So, when a 2MB page is used, even pounding on a single byte out of that 2MB region will classify the complete 2MB region as hot. Although 99% of the bytes are cold and could have been potentially mapped to slow memory. Therefore, we have a problem in detecting true cold pages at 2MB granularity.

## Slide 97: How much slowdown is tolerable?
Server CapEx ~ 17%
If slow memory is 1/3 as cheap as DRAM, overall cost saved ~ 3%
Less perf  more servers, slowdown of x%  x% higher TCO
Can only have at most 3% slowdown
Source: The Datacenter as a Computer: An Introduction to the Design of Warehouse-Scale Machines, Second Edition, Luiz André Barroso, Jimmy Clidaras, Urs Hölzle, 50% occupied datacenter scenario, pp. 97
Notes: But how much slowdown can we actually tolerate without increasing the overall cost of deployment. On the right we have a pie chart of TCO distribution for a 50% occupied data center. We see that capital expenditure is 17% of the overall cost. So, if slow memory is 1/3 as cheap as DRAM then overall cost saved will be 3% assuming memory cost is 30% of the machine cost. But less performance means more servers to maintain same level of throughput. Therefore, we can have at most 3% slowdown in order to reduce total cost of ownership.

## Slide 98: Thesis statement
Study memory characteristics beyond memory access latency
Goals:
Simplify system design
Ease programmability (application-transparent policies)
Increase performance / unit cost
Efforts driven towards adoption in production systems

## Slide 99: Different memory technologies
Memory Technology ↓ | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
GDDR / HBM | 1x | 2-8x | 2x | 2x
3D XPoint | 4-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
LPDDR | 1x | 1x | x/4 | x/2
Notes: Leaving capacity for now

## Slide 100: Different memory technologies
How to exploit characteristics of different memory technologies?
Memory Technology ↓ | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
GDDR / HBM | 1x | 2-8x | 2x | 2x
3D XPoint | 4-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
LPDDR | 1x | 1x | x/4 | x/2
High bandwidth memory
Cheaper slower memory
2-8x
4-10x
x/2 – x/5
x/2
Low power memory
Notes: Verify above numbers
Remove LPDDR numbers
Leaving capacity for now

## Slide 101: My proposal: BW-AWARE placement
Place data in the ratio of the memory bandwidths
Utilize bandwidth of all the available memory zones
Chart: Ratio of Pages Placed in Graphics (G):CPU (C) Memory
| 100G-0C | 90G-10C | 80G-20C | 70G-30C | 60G-40C | 50G-50C | 40G-60C | 30G-70C | 20G-80C | 10G-90C | 0G-100C
Average across General Purpose GPU Applications | 1.1265 | 1.2071 | 1.2869 | 1.3343 | 1.1484 | 1 | 0.86974 | 0.77128 | 0.69057 | 0.62381 | 0.56707
BW-AWARE placement maximizes BW hence the GPU throughput
Higher is better
Graphics : CPU memory BW ratio: 2.5 : 1
Notes: Proposal??

## Slide 102: My proposal: BW-AWARE placement
Place data in the ratio of the memory bandwidths
  Utilize bandwidth of all the available memory zones
Chart: Ratio of Pages Placed in Graphics (G):CPU (C) Memory
| 100G-0C | 90G-10C | 80G-20C | 70G-30C | 60G-40C | 50G-50C | 40G-60C | 30G-70C | 20G-80C | 10G-90C | 0G-100C
Average across General Purpose GPU Applications | 1.1265 | 1.2071 | 1.2869 | 1.3343 | 1.1484 | 1 | 0.86974 | 0.77128 | 0.69057 | 0.62381 | 0.56707
BW-AWARE placement maximizes BW hence the GPU throughput
Higher is better
Graphics : CPU memory BW ratio: 2.5 : 1
GPU
CPU
Dedicated CPU-GPU Link
Unified Memory
DDR4
DDR4
DDR4
CPU
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
BW: 1x
BW: 1x
BW: 2.5x
70% data here
30% data here
Notes: Proposal??

## Slide 103: My proposal: Selective GPU caching
GPU caches only if CPU is not caching, GPU is latency tolerant
CPU and GPU cache coherence protocols need not be the same
Chart: Performance wrt HW CC
| Naive Selective Caching | L1L2-MSHR Coalescing | 512KB-Client Cache | Variable size transfers
 | 0.42 | 0.799 | 0.8977 | 0.927
With SW protection, performance at par with HW cache coherence
Average across General Purpose GPU Application
Higher is better
HW cache coherence
✔High Performance
❌High design complexity
Selective GPU caching
✔ High performance
✔ Low design complexity

## Slide 104: My proposal: Selective GPU caching
GPU caches only if CPU is not caching, GPU is latency tolerant
CPU and GPU cache coherence protocols may not be the same
Chart: Performance wrt HW CC
| Naive Selective Caching | L1L2-MSHR Coalescing | 512KB-Client Cache | Variable size transfers
 | 0.42 | 0.799 | 0.8977 | 0.927
93%
With SW protection, performance at par with HW cache coherence
Average across General Purpose GPU Application
Higher is better

## Slide 105: Cheaper memory technologies
Memory Technology ↓ | Access latency | Bandwidth | Cost / bit | Energy / bit
DDR | 1x | 1x | 1x | 1x
3D XPoint | 5x-10x | x/2- x/4 | x/3 – x/5 | x/2 – x/4
hot data
cold data
CPU
DDR4
DDR4
DDR4
DDR
50-100ns
Future
CPU
DDR4
DDR
DDR4
DDR4
DDR4
XPoint
10x slower than DDR
50-100ns
Fast memory
Cheaper/slower memory
Mapping cold data to slow memory will free DRAM for other apps
Notes: Animation not that clear
However, with cheaper slower memory we can leverage the difference between data access frequency and place hot pages in fast DRAM and cold pages in cheaper/slower memory. Thus, there is an opportunity to cut down the DRAM requirement per application. Note that we only want to place those pages in slow memory that will not degrade application performance leading to SLA violations.

## Slide 106: How to reduce memory spending?
Application Pages
Thermostat: Increase perf/$ with cheaper memories [ASPLOS’17]
  Satisfy application performance requirements (eg., SLAs)
  Exploit performance benefit of huge pages
System administrator specifies:
tolerable slowdown
Thermostat
in OS
DRAM
Slow Mem
Up to 50% data in slow memory with <= 3% slowdown
for NoSQL databases, TPCC, data analytics

## Slide 107: CPU-GPU coherence impacting
void gpuFunction(int *gpu_data,
int *status) {
...;
status = 1;
}
int main() {
int *gpu_data = malloc(1000);
int status = 0;
bool done = false;
// GPU behaves almost like a thread
gpuFunction<<<...>>>(gpu_data,
&status);
// Check if computation is done.
while(!status) {
sleep(1);
}
}
void gpuFunction(int *gpu_data,
int *status) {
...;
status = 1;
}
int main() {
// Need to cudaMalloc() instead of malloc()
int *gpu_data = cudaMalloc(1000);
int status = 0;
gpuFunction<<<...>>>(gpu_data,
&status);
// Can’t simply view kernel progress.
cudaDeviceSync();
cudaSync();
}

## Slide 108: REmove: Contribution: Thermostat
Application-transparent, huge-page-aware mechanism
Cold data in slow memory while satisfying perf. requirements
Low-overhead sampling to estimate page access rates
Prototyped in Linux 4.5
Places up to 50% of application footprint in cheaper/slower memory while satisfying 3% tolerable slowdown
[Agarwal ASPLOS’17]
Notes: Thus we design Thermostat, an application-transparent

## Slide 109: CPU-GPU cache coherence
GPU
CPU
Dedicated CPU-GPU Link
Unified Memory
DDR4
DDR4
DDR4
CPU
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
CPU memory
DDR technology
Graphics memory
GDDR/HBM technology
(higher bandwidth)
Coral system (IBM cpu, NVIDIA gpu)
Page
Line
Cache coherence
Improves programmer productivity
Improves performance via fine-grained access to CPU memory
But, hard to implement
  Design complexity
  Vendor collaboration
Notes: in CPU coherence,
GPU: graphics, GPGPU
story: from CPU -> GPU
Replace this animation with a code example

## Slide 110: Issues with existing cold page detection
Not governed by application performance requirements
Cranking up scanning frequency eats up slowdown budget
  Perf loss due to frequent TLB flushing, more on virtualized platforms
Goal: Low-overhead mechanism to detect cold pages
while satisfying performance requirements

## Slide 111: Adoption in production system
Selective caching
  NVLink 2.0 supports variable link transfers
  Ideas to be implemented in IBM & NVIDIA collaborated for Coral system
REMOVE: Page placement/migration policies
  Prefetching policies to be supported by unified virtual memory (UVM)
Notes: When is coral supposed to come out?
Maybe remove this slide

## Slide 112: CPU-GPU heterogeneous systems
GPU
CPU
CPU-GPU Link
Unified Memory
DDR4
DDR4
DDR4
CPU
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
CPU memory
DDR technology
Graphics memory
GDDR/HBM technology
(higher bandwidth)
Coral system (IBM cpu, NVIDIA gpu)
What is new with CPU-GPU heterogeneous systems?
CPU-GPU Link
Conventional: PCIe
Higher latency (1-10us)
Lower bandwidth (~16GB/s)
All GPU data is placed in graphics memory
Upcoming: NVLink
Lower latency (~100ns)
Higher bandwidth (80GB/s)
GPU can access CPU memory at much higher BW & lower latency
Notes: NVLink is cache coherent
R1, R2, R3?

## Slide 113: Contribution: BW-AWARE placement
Chart: Throughput Normalized
| Local placement | Interleave placement | BW-AWARE placement
Average across General Purpose GPU Applications | 1 | 0.89286 | 1.1964
Place data in the ratio of the memory bandwidths
  Utilize bandwidth of all the available memory zones
BW-AWARE placement maximizes BW hence the GPU throughput
Better
GPU
CPU
DDR4
DDR4
DDR4
CPU
memory
DDR4
DDR4
DDR4
DDR4
DDR4
DDR4
Graphics memory
BW: 1x
BW: 1x
BW: 2.5x
Average across General Purpose GPU Apps
Data in CPU memory | Data in Graphics memory | Policy
0 | 100% | Local
50% | 50% | Interleave
30% | 70% | BW-AWARE
[Agarwal ASPLOS’15]