## Slide 1: Heterogeneous Memory Management
Neha Agarwal
December 18, 2015
Thesis Proposal

## Slide 2: Conventional Memory Hierarchy
CPU
Memory (DDR)
GPU
Memory (GDDR)

## Slide 3: Heterogeneous Memory Systems
CPU
Memory
(DDR)
Memory
(XPoint)
GPU
Memory
(GDDR)
Memory
(DDR)
Different Coherence Domain
↓ Latency
↓ Cost per bit
↑ Bandwidth

## Slide 4
Optimized for latency
Core
Memory

## Slide 5: Wait, but...
What about bandwidth to my GPU?
What about cost/bit in my data-center?
Optimized for latency
Core
Memory

## Slide 6: My Thesis
Bandwidth
Coherence Domain
Costs/bit
Memory management accounting differences in memory technologies
Application transparent
Equips OS/Programmer
Dynamic decisions at runtime

## Slide 7: My Contributions
BW-AWARE placement for bandwidth maximization in GPUs, +35% over Linux Interleave placement
Dynamic page migration for GPU with range expansion and bandwidth balancing, +6% over Legacy CUDA
Selective Caching for CC-NUMA CPU-GPU systems to simply coherence, 93% of hardware cache-coherent system

## Slide 8: Proposal: Thermostat
Huge page aware, application transparent data placement in 2-tiered memory system

## Slide 9: Talk Outline
Bandwidth maximization in GPUs
Eliminating CPU-GPU Cache Coherence
Proposal: Thermostat

## Slide 10: Bandwidth Maximization in GPUs
Agarwal, N., Nellans, D., O'Connor, M., Keckler, S. W., & Wenisch, T. F. (2015, February). Unlocking bandwidth for GPUs in CC-NUMA systems. In High Performance Computer Architecture (HPCA), 2015 IEEE 21st International Symposium on (pp. 354-365).
Agarwal, N., Nellans, D., Stephenson, M., O'Connor, M., & Keckler, S. W. (2015, March). Page Placement Strategies for GPUs within Heterogeneous Memory Systems. In Proceedings of the Twentieth International Conference on Architectural Support for Programming Languages and Operating Systems (pp. 607-618).

## Slide 11: GPU Workloads: Memory Bandwidth Sensitive
Chart: Aggregate DRAM Bandwidth, 1x=200GB/sec
| 0.125x | 0.25x | 0.5x | 1x | 2x | 3x
backprop | 0.16289 | 0.31884 | 0.59656 | 1 | 1.279 | 1.3221
bfs | 0.12978 | 0.25839 | 0.51495 | 1 | 1.587 | 1.5942
btree | 0.31648 | 0.55795 | 0.86131 | 1 | 1.0178 | 1.0237
cfd | 0.12522 | 0.25043 | 0.50087 | 1 | 1.9409 | 2.4243
gaussian | 0.54999 | 0.8 | 0.9444 | 1 | 1.0522 | 1.0521
heartwall | 0.44969 | 0.7066 | 0.90716 | 1 | 1.034 | 1.0379
hotspot | 0.24984 | 0.47593 | 0.83258 | 1 | 1.0152 | 1.0152
kmeans | 0.14071 | 0.28109 | 0.56251 | 1 | 1.2648 | 1.272
lava_MD | 1.0007 | 0.99539 | 1.008 | 1 | 0.99388 | 1.0008
leukocyte | 0.90083 | 0.91786 | 0.99843 | 1 | 0.99807 | 1
lud_cuda | 0.96778 | 0.98949 | 0.99786 | 1 | 1.0006 | 1.0019
mummergpu | 0.13794 | 0.27494 | 0.54339 | 1 | 1.2554 | 1.2398
Applications perform up to 2.8x better with 3x more BW
Notes: In order to understand why utilizing CC-BW is crucial to the GPU performance, let us look at the sensitivity of GPU applications to the memory BW.
Explain the graph
Hence it is imperative to exploit as much BW as possible in order to get the best possible performance for most of the GPU workloads.

## Slide 12: GPU Workloads: Memory Latency Tolerant
Applications are more sensitive to memory bandwidth than latency
Chart: DRAM Latency (cycles), Baseline ≈ 100 cycles
| 1.0 | 20.0 | 40.0 | 60.0 | 80.0 | 100.0 | 120.0 | 140.0 | 160.0 | 180.0 | 200.0
backprop | 1.049 | 1.0429 | 1.0297 | 1.017 | 1.0094 | 1 | 0.98338 | 0.97417 | 0.95656 | 0.94446 | 0.93499
bfs | 1.0139 | 1.0097 | 1.0066 | 1.0048 | 1.002 | 1 | 0.99751 | 0.99579 | 0.99229 | 0.99142 | 0.9895
btree | 1.0889 | 1.0755 | 1.0613 | 1.0433 | 1.0222 | 1 | 0.9814 | 0.95717 | 0.93945 | 0.91544 | 0.89503
cfd | 1.004 | 1 | 1.0162 | 1.0223 | 1.0142 | 1 | 1.004 | 1.0162 | 1.0142 | 1 | 1.0081
gaussian | 1.1181 | 1.0936 | 1.068 | 1.0443 | 1.0217 | 1 | 0.97891 | 0.95837 | 0.93918 | 0.92086 | 0.90322
heartwell | 1.001 | 1.0019 | 1.0015 | 1.0017 | 0.99936 | 1 | 1.0012 | 1.0013 | 0.99887 | 0.99887 | 0.99833
hotspot | 1.0189 | 1.0219 | 1.0149 | 1.0045 | 1.0024 | 1 | 0.98987 | 0.98118 | 0.97478 | 0.96943 | 0.9641
kmeans | 1.0048 | 1.0037 | 1.003 | 1.0026 | 1.0016 | 1 | 0.99799 | 0.997 | 0.99544 | 0.9934 | 0.99302
lava_MD | 1.02 | 1.0164 | 1.031 | 1.0158 | 1.0217 | 1 | 0.99183 | 0.99183 | 1.0207 | 0.99183 | 1.0362
leukocyte | 1.0012 | 1.0016 | 1.0014 | 0.99922 | 0.9991 | 1 | 0.99861 | 0.9997 | 0.99842 | 1.0001 | 0.99863
lud_cuda | 1.01 | 1.0083 | 1.0068 | 1.0049 | 1.0024 | 1 | 1.0003 | 0.9976 | 0.99697 | 0.9912 | 0.99155
mummergpu | 0.99952 | 1.0016 | 1.0023 | 1.0009 | 1.0044 | 1 | 1.0008 | 0.99302 | 0.99043 | 0.99657 | 0.98713
Notes: However, we observed that most of these workloads are tolerant to memory latency.
Explain the graph
All except one are tolerant to memory latency
Hence, we can see that memory bandwidth is a better dictator of GPU application performance than main memory latency. Hence it is important to exploit the BW available through CC-interconnect to maximize performance although those memory access will have higher latencies.

## Slide 13: Evolving GPU Memory System
CUDA 1.0-5.x
CUDA 6.0+: Current
Future
cudaMemcpy
Programmer controlled copying to GPU memory
Unified virtual memory
Run-time controlled copying 
Better productivity
CPU-GPU cache-coherent
high BW interconnect
How to best exploit full BW while maintaining programmability?
Roadmap
GDDR5
GPU
CPU
200 GB/s
80 GB/s
80 GB/s
NVLink
(Cache Coherent)
PCI-E
15.8 GB/s
DDR4
Notes: Let me first take you through the evolution of GPU memory system via a roadmap.
A typical CPU-GPU system today is connected by a PCI-E link. The GPU is connected to high bandwidth GDDR memory and CPU is connected to high-capacity but lower-bandwidth DDR memory.
Example system
In the legacy systems from first generation of CUDA uptill CUDA 5, programming model was such that GPU could only access the GDDR memory attached to it. Programmer was responsible to identify the data accessed by the GPU and manually transfer it to the GDDR memory using cudaMemcpy calls. Such a programming model demands high effort on part of the programmer.
Moving forward CUDA 6.0 onwards Unified virtual memory was introduced, wherein the programmer is no longer required to make explicit data copies. Using the same hardware as in the legacy systems runtime software performs on-demand data copying to the GPU memory. Although this memory abstraction had a significant impact on improving programmer productivity still on-demand copying slows down the running program.
Moving further ahead, we anticipate that CPU & GPU will become cache coherent. As announced by the GPU vendors CPU & GPU will be connected via a high BW interconnect such as NVIDIA’s NVLink. For the first time GPU will be able to transparently access the CPU memory. This future system provides various opportunities for performance enhancement as GPU can now use BW from both CPU and GPU memories. The big question here is how to exploit the full system BW in the best possible way without burdening the programmer to worry about the data placement or copying decisions.
Goals:
Simple programming model
Exploit full DDR + GDDR BW

## Slide 14: GPU Bandwidth Utilization
% of Migrated Pages to GPU Memory
DDR4
GDDR5
GPU
CPU
200 GB/s
80 GB/s
NVLink
80 GB/s
Coherence-based accesses, wastes GPU memory BW
80
200
280
GPU Memory BW
Total System Memory BW
Total Bandwidth (GB/s)
0
100
Additional BW from CC
Notes: Now, let us look at the BW utilization as we start running an application on this system. On the left we will see how GPU accesses the data from the memory system and on the right we will see the BW utilization for those accesses.
For the sake of the programmability, all the data is allocated in the CPU memory to begin with. GPU can access this data from the CPU memory via cache coherence. Hence, the best BW utilization in such topology can be only 80GB/s, which is only 30% of the total system BW. We are not able to use 70% of the system BW which a a big lose from performance perspective.
With no page migrations this system will end up wasting high BW GPU memory.
Next, we move onto the future CC-NUMA system where CPU and GPU are connected through a high BW interconnect of 80GB/s. For the sake of programmability all the data structures reside in the CPU memory to start with. GPU can do coherence-based accesses and thus the total BW utilizes in this system will be 80GB/s. Clearly, with no page migration enabled from DDR to GDDR memory this system will end up wasting high BW GPU memory.

## Slide 15: GPU Bandwidth Utilization
DDR4
GDDR5
GPU
CPU
200 GB/s
80 GB/s
NVLink
80 GB/s
Bandwidth-Aware Placement
Place data in the ratio of memory bandwidths
80
200
280
Additional BW from CC
GPU Memory BW
Total System Memory BW
% of Migrated Pages to GPU Memory
Total Bandwidth (GB/s)
0
100
70
Notes: Remember, our goal here is to reach the peak BW as soon as possible. As pages are migrated to the GPU memory BW utilization will go up. We have observed that the best bandwidth utilization happens when the application data is spread across the GDDR and DDR memories in the ratio of their bandwidths. In our ASPLOS 2015 paper we will discuss more about the static placement policies. The goal of this work however is to dynamically migrate pages so that data is divided in the ratio of memory BW and thus GPU can concurrently access both the memories.
Distinguish ASPLOS from HPCA
Correct animation
How can we utilize both the CPU and the GPU memory BW? In our ASPLOS 2015 paper we will discuss about the static oracle placement that achieves the goal of maximizing BW utilization from both the memories. By placing data in the ratio of memory BW here it being 70:30% GPU can saturate both the memories and thus achieve the cumulative BW of 280GB/s. The goal of this work is to achieve this static oracle performance by dynamically migrating pages among DDR and GDDR memories.

## Slide 16: GPU Bandwidth Utilization
% of Migrated Pages to GPU Memory
GDDR5
GPU
CPU
200 GB/s
80 GB/s
NVLink
80 GB/s
DDR4
80
200
280
Additional BW from CC
GPU Memory BW
Total System Memory BW
Total Bandwidth (GB/s)
0
100
Excessive data in GDDR leads to under-utilization of DDR BW
70
Notes: As more and more migration happen, a point comes where all the data is transferred to the GPU memory. In such a case GPU memory requests can only be served from GDDR memory. Excessive page migration leads to under-utilization of the CPU memory BW. Hence page migration policy should only migrate pages to unlock memory BW of both the DDR and the GDDR memories.
So, the take away from the above discussion is that we want to utilize both 200GB/s from GDDR memory and 80GB/s from DDR memory at the same time we do not programmer to worry about these decisions.
Let us try to understand how BW is utilized in the Legacy/Current CPU-GPU systems where either programmer/SW runtime copies data accessed by the GPU to the GDDR memory.
On the left we can see a GPU attached to the CPU through low BW PCI-E link. Any data accessed by the GPU has to be placed in the GDDR memory as this system is not CC, which means that DDR BW will not be used by the GPU. All the GPU accesses happen through 200GB/s attached memory. Therefore, the total BW utilization of this topology can be 200GB/s.

## Slide 17: BW Maximization Policies
BW-AWARE Placement
  Place pages in the ratio of memory bandwidths
  Application agnostic policy
Dynamic Page Migration
  Aggressively migrate pages upon First-Touch to GDDR memory
  Pre-fetch neighbors of touched pages to reduce TLB shootdowns
  Throttle page migrations when nearing peak BW
Notes: In this work, we have developed intelligent dynamic page migration policies that demands no programmer involvement. We aggressively migrate pages to the GDDR memory after a page has been accessed. We employ a technique to pre-fetch neighbors of already accessed pages to reduce TLB shootdowns. Finally, we throttle page migrations when BW utilization peaks as more migration lead to under-utilization of the CPU memory BW.
Our dynamic page migration policy performs 1.95 times better than no migration case, is within 28% of the static oracle performance and is 6% better than the Legacy CUDA.

## Slide 18: Simulation Environment
Simulator: GPGPU-Sim 3.x
Heterogeneous 2-level memory
  GDDR5 (200GB/s, 8-channels)
  DDR4 (80GB/s, 4-channels)
GPU-CPU interconnect
  Latency: 100 GPU core cycles
Workloads:
  Rodinia applications [Che’IISWC2009]
  DoE mini apps [Villa’SC2014]
GDDR5
GPU
CPU
200 GB/s
80 GB/s
100 clks additional latency
80 GB/s
DDR4

## Slide 19: BW-AWARE Placement Performance
Chart: Ratio of Pages Placed in GDDR:DDR Memories
| 100G-0D | 90G-10D | 80G-20D | 70G-30D | 60G-40D | 50G-50D | 40G-60D | 30G-70D | 20G-80D | 10G-90D | 0G-100D
backprop | 1.0121 | 1.1065 | 1.1962 | 1.2717 | 1.1342 | 1 | 0.82302 | 0.7157 | 0.63775 | 0.57494 | 0.52603
bfs | 1.3001 | 1.4755 | 1.6365 | 1.8425 | 1.3401 | 1 | 0.7764 | 0.62929 | 0.53022 | 0.45746 | 0.40256
cfd | 1.0285 | 1.0795 | 1.1253 | 1.1616 | 1.0949 | 1 | 0.90911 | 0.84854 | 0.78224 | 0.73101 | 0.69327
gaussian | 1.0205 | 1.056 | 1.0898 | 1.107 | 1.0772 | 1 | 0.91729 | 0.84263 | 0.77721 | 0.71791 | 0.66211
kmeans | 1.2549 | 1.3591 | 1.488 | 1.4746 | 1.1995 | 1 | 0.85941 | 0.74471 | 0.64557 | 0.56352 | 0.49701
mummergpu | 1.2868 | 1.4074 | 1.5544 | 1.5901 | 1.2489 | 1 | 0.82479 | 0.69499 | 0.59924 | 0.52765 | 0.47157
needle | 1.065 | 1.1019 | 1.1337 | 1.1362 | 1.084 | 1 | 0.92089 | 0.84129 | 0.76858 | 0.70492 | 0.64676
nn | 1.1969 | 1.194 | 1.204 | 1.2151 | 1.0387 | 1 | 0.8565 | 0.70637 | 0.65701 | 0.58506 | 0.52088
pathfinder | 0.98929 | 1.0045 | 1.0147 | 1.0177 | 1.0185 | 1 | 0.93752 | 0.84279 | 0.75939 | 0.682 | 0.61681
srad_v1 | 1.0867 | 1.1826 | 1.2889 | 1.3915 | 1.1933 | 1 | 0.86256 | 0.75556 | 0.67469 | 0.60643 | 0.54944
cns | 0.99014 | 1.0552 | 1.1208 | 1.1483 | 1.142 | 1 | 0.88393 | 0.76977 | 0.69398 | 0.62058 | 0.56752
comd | 0.99074 | 0.99749 | 1.0003 | 1.002 | 1.0044 | 1 | 0.99386 | 0.97618 | 0.87941 | 0.79545 | 0.66255
35% better than INTERLEAVE, 18% better than LOCAL
Notes: Latency sensitive app (sgemm)
  Performance degraded

## Slide 20: Dynamic Page Migration
Chart: Throughput Relative to No Migration
| backprop | bfs | cns | comd | kmeans | minife | mummer | needle | pathfinder | srad_v1 | xsbench | geo-mean
Legacy CUDA | 1.2456 | 3.0805 | 1.7139 | 1.4954 | 2.525 | 1.7619 | 2.7028 | 1.3362 | 0.91416 | 1.9765 | 3.1966 | 1.8583
First-Touch + Range Exp + BW Balancing | 1.3384 | 4.14 | 2.588 | 1.4709 | 2.67 | 0.97576 | 2.0535 | 1.7 | 1.0729 | 2.1574 | 3.5 | 1.9505
ORACLE | 2.4175 | 4.577 | 3.23 | 1.5124 | 2.9669 | 2.9856 | 3.3718 | 1.7567 | 1.65 | 2.5326 | 5.6126 | 2.7444
6% better than Legacy CUDA
Static Oracle
Notes: Nevertheless

## Slide 21: Eliminating CPU-GPU Cache Coherence
Agarwal, N., Nellans, D., Ebrahimi, E., Wenisch, T. F., Danskin, J., & Keckler, S. W. (2016, March). Selective Caches in GPUs to Eliminate Cache Coherence. To appear in High Performance Computer Architecture (HPCA), 2016 IEEE 22nd International Symposium.

## Slide 22: HW Cache Coherence: Liability for CPU-GPU Systems
Goal: Shared virtual address space with performance & programmability
Notes: Why do we need cache coherence?

## Slide 23: Selective GPU Caches
Provides unified shared memory w/o HW cache-coherence
GPU does not cache any data actively used by the CPU
  Insensitive to memory access latency
Micro-architectural enhancements to make system performant

## Slide 24: Principles Of Selective Caching
GPU writes DDR:
DIR handles invalidation of CPU caches
CPU reads/writes GDDR:
Line inserted in Remote Directory (Filter) GPU can’t cache lines found in this filter
Directory
CPUs
Remote Directory
GPU reads DDR:
DIR sends most recent copy
DDR4
DDR4
DDR4
DDR4
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GPU
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Notes: Remote Directory Implementation

## Slide 25: Principles Of Selective Caching
GPU writes DDR:
DIR handles invalidation of CPU caches
CPU reads/writes GDDR:
Line inserted in Remote Directory (Filter) GPU can’t cache lines found in this filter
Directory
CPUs
Remote Directory
GPU reads DDR:
DIR sends most recent copy
DDR4
DDR4
DDR4
DDR4
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GPU
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Notes: Remote Directory Implementation

## Slide 26: Request Coalescing
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Coalesces GPU requests to DDR
Directory
CPUs
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
DDR4
DDR4
DDR4
DDR4
GPU
u
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5

## Slide 27: Request Coalescing
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Coalesces GPU requests to DDR
Directory
CPUs
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
DDR4
DDR4
DDR4
DDR4
GPU
u
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5

## Slide 28: CPU-side Client Cache
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Coalesces GPU requests to DDR
Directory
CPUs
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
DDR4
DDR4
DDR4
DDR4
GPU
u
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Reduces DDR traffic from the GPU
Client Cache
v

## Slide 29: CPU-side Client Cache
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Coalesces GPU requests to DDR
Directory
CPUs
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
DDR4
DDR4
DDR4
DDR4
GPU
u
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Reduces DDR traffic from the GPU
Client Cache
v

## Slide 30: Variable Width Request Transfer
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Coalesces GPU requests to DDR
Directory
CPUs
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
DDR4
DDR4
DDR4
DDR4
GPU
u
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Reduces DDR traffic from the GPU
Client Cache
v
Variable-size Transfer
Improves CPU-GPU interconnect efficiency
w

## Slide 31: Variable Width Request Transfer
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Coalesces GPU requests to DDR
Directory
CPUs
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
DDR4
DDR4
DDR4
DDR4
GPU
u
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Reduces DDR traffic from the GPU
Client Cache
v
Variable-size Transfer
Improves CPU-GPU interconnect efficiency
w

## Slide 32: Lots of Read-only Data
62% data is read-only

## Slide 33: Request Coalescing
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Reduces DDR traffic from the GPU
Coalesces GPU requests to DDR
Directory
CPUs
Client Cache
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
Read-only Cache
DDR4
DDR4
DDR4
DDR4
GPU
Variable-size Transfer
Provides safe caching
Improves CPU-GPU interconnect efficiency
u
w
v
x
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5

## Slide 34: Selective Caching In A Nutshell
CPU caches all memory
GPU caches GPU-memory if CPU not caching
GPU never caches CPU-memory
Reduces DDR traffic from the GPU
Coalesces GPU requests to DDR
Directory
CPUs
Client Cache
Request Coalescer
CPU/GPU reads DDR:
GPU caches until 1st write to the page
CPU/GPU writes DDR:
Flush read-only pages in GPU caches
and updates page level protection
Read-only Cache
DDR4
DDR4
DDR4
DDR4
GPU
Variable-size Transfer
Provides safe caching
Improves CPU-GPU interconnect efficiency
u
w
v
x
Remote Directory
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
GDDR5
Micro-architectural enhancements: 93% of HW cache-coherence performance

## Slide 35: Conclusion: CPU-GPU Systems
BW-AWARE placement maximizes GPU bandwidth utilization
Dynamic page migration: performance with programmability
Selective caching simplifies unified shared memory
  Decouples vendor-specific coherence protocols

## Slide 36: Proposal: Thermostat
Managing Huge Pages in Two-Tiered Memory in Data-centers

## Slide 37
Data-center Memory TCO
30%

## Slide 38: New Memory Technology ½ DRAM Cost ~4x Slower than DRAM
Data-center Memory TCO
30%

## Slide 39: Reduce Data-center Memory TCO && Service Level Guarantees

## Slide 40: What’s new with 2-Tier Memory?
Huge Pages

## Slide 41: Huge Pages – Improve Performance
Regular OS pages: 4KB, Huge pages: 2MB
Advantages:
  Fewer TLB misses
  Faster TLB misses (3-level lookup instead of 4)
Performance gain of 10-15% with huge pages
Notes: THP – Available today in Linux kernel

## Slide 42
BUT

## Slide 43: Problem: Huge Pages in 2-Tier Memory
Reduces fraction of cold data to be put into slow memory
Expensive to migrate data at 2MB granularity

## Slide 44: Thermostat – Make Slow Memory Usable in Data-centers
Detect cold pages
Hot spots in otherwise cold huge pages
Multiple page mappings to fast and slow memory

## Slide 45: Future Memory Hierarchy
Fast Memory
(DRAM)
Slow Memory
(3D X Point)
100 ns
500 ns – 1us
CPU
Hot Data
Cold Data

## Slide 46: Cold Data Slow Memory
Identified cold data at runtime using “kstaled” in Linux kernel
~50% of cold 4KB pages can go to slow memory
Chart: % of Pages Idle for half a minute
| redis | cassandra
4KB Pages | 65.2174 | 46.6667

## Slide 47: Cold Data Slow Memory
Cold page fraction reduces from 50% to 15%
Chart: % of Pages Idle for half a minute
| redis | cassandra
2MB Pages | 9.8 | 23.0769
4KB Pages | 65.2174 | 46.6667

## Slide 48: Problem: Identify HotSpots in Cold Huge Pages
Separate 4KB hot pages within 2MB huge page

## Slide 50: Identifying HotSpot Huge Pages
Online sampling mechanism

## Slide 51: Identifying HotSpot Huge Pages
Online sampling mechanism
Hot Huge Page
Cold Huge Page
HotSpot Huge Page

## Slide 52: Future Memory Hierarchy
500 ns – 1us
Fast Memory
(DRAM)
Slow Memory
(3D X Point)
100 ns
500 ns – 1us
CPU
Hot Huge Page + Hot 4KB
Cold + HotSpot Huge Pages

## Slide 53: Amount of cold data cdf

## Slide 54: Multiple Memory Mappaings
Have 2 valid mappings for a page,
4KB mapping and 2MB mapping
...
Bit vector to validate 2MB mapping
If valid use 2MB mapping, else fetch 4KB mapping from memory

## Slide 55: In Summary – Thermostat
Reaps benefits of huge pages while reducing memory cost in data-centers
Places cold pages in slow memory
Identifies HotSpots huge pages & puts their cold regions in slow memory
Translation facades keep hot 4KB pages in fast DRAM